25 HOUR INSPECTION GUIDE

| Component | Action | Initial |
| --- | --- | --- |
| Engine | Remove left and right cowling |  |
|  | Clean |  |
|  | Inspect for fuel and oil leaks. |  |
|  | Check for security and condition of all equipment in accessory section. |  |
| Starter Drive | Lube - Graphite & Kerosene |  |
| Air Filter | Remove, Inspect, and Clean |  |
| Battery | Access through large empennage opening Check Fluid Level |  |
| Tires | Check condition and tire pressure |  |
| Retractable Step | Lube - Tri-Flow Teflon lubricant |  |
| Instrument Panel | Check all instruments for operation, dials for proper markings, and placards for legibility. |  |
| Pitot static system | Check static and pressure system for leaks or stoppage. |  |
| Exterior | Inspect general condition for missing screws, bolts, nuts, etc. |  |

COMMENTS: