50 HOUR INSPECTION GUIDE

| Component | Action | Initial |
| --- | --- | --- |
| 25 Hour Inspection Items: |
| Engine | Remove left and right cowling |  |
|  | Clean |  |
|  | Inspect for fuel and oil leaks. |  |
|  | Check for security and condition of all equipment in accessory section. |  |
| Starter Drive | Lube - Graphite & Kerosene |  |
| Air Filter | Remove, Inspect, and Clean |  |
| Battery | Access through large empennage opening Check Fluid Level |  |
| Tires | Check condition and tire pressure |  |
| Instrument Panel | Check all instruments for operation, dials for proper markings, and placards for legibility. |  |
| Pitot static system | Check static and pressure system for leaks or stoppage. |  |
| Exterior | Inspect general condition for missing screws, bolts, nuts, etc. |  |

| Component | Action | Initial |
| --- | --- | --- |
| Additional Items for 50 Hour Inspection: |
| Engine | Drain Oil, Replace Filter |  |
|  | Check engine for oil leaks |  |
|  | Check ignition harness for fray, wear, etc. |  |
|  | Check throttle, mixture, and prop. Governor control for general condition, travel, and free operation. |  |
|  | Check engine mount structure and engine rubber dynafocal mounts |  |
|  | Check engine stacks for general condition |  |
|  | Check engine baffles for wear and cracks. |  |
|  | Check fluid in brake reservoir. |  |
|  | Check battery and cables |  |
|  | Check cowl for cracks, loose or missing screws, etc. |  |
| Propeller | Remove and inspect spinner. |  |
|  | Check propeller for oil leaks and general condition. |  |
|  | Inspect blades for nicks and cracks. |  |
|  | Clean and reinstall spinner. |  |
| Cabin | Check parking brake cylinder for leaks. |  |
|  | Check trim operation. |  |
|  | Check cabin door and pilot window for damage and proper operation. |  |
|  | Check cabin, navigation, instruments, and landing lights. |  |
|  | Check fuel selector valve for proper operation. |  |
| Landing Gear | Check tires for freedom from excessive wear and proper inflation (Refer to Section 1 page 1-5). |  |
|  | Check for general condition. |  |
|  | Check collars and bolts for damage (Refer to Section V-G). |  |
| Wing | Check surfaces and tips for damage. |  |
|  | Check ailerons, aileron attachments, and bell cranks for damage and operation. |  |
|  | Check flaps and attachments for damage and operation. |  |
| Fuselage and Empennage | Check stabilizer, fin, and rudder surfaces for damage. |  |
|  | Check rudder and elevators for proper attachment. |  |

50 HOUR LUBRICATION GUIDE

| Component | Action | Initial |
| --- | --- | --- |
| Hydraulic Reservoir | Top off with MIL-H-5606 Red Hydraulic fluid |  |
| Nose Gear Doors | Rod End Bearings - Lube with Tri-Flow Teflon Spray |  |
| Main Gear Doors | Rod End Bearings - Lube with Tri-Flow Teflon Spray |  |
| Brakes | Pressure Plate Anchor Bolts – Lube with Tri-Flow Teflon Spray. |  |